The details from the motor controller data sheet are:

I am changing these to:
1. 0 (no change)
2. 1 (no change)
3. 0 (no change)
4. 1 (CHANGED)
5. 1 (CHANGED)
6. 200 (CHANGED)
7. 200 (CHANGED)
8. 1 (no change)
9. 20 (no change)
10. 1 (no change)
11. 35 (no change)
12. 0 (no change)
13. 0 (no change)
14. 0 (no change)
15. 5 (CHANGED)
16. 5 (CHANGED)
17. 0 (no change)

These put the unit into a mode where the FWD line is 0 for reverse and 1 for forward and the speed is controlled by the ADC on SPEED-2 line. (parameters 4/5)

Parameters 6/7 set the current limit for overcurrent. This is 200 = 20.0A and is the highest. This might need to be changed in the future.

Parameters 15/16 are changed to 5 to give very fast slow down to stop limits switches being hit too hard.