Changes made to reverse the motor direction (due to gear changing direction):

1. On Motor controller: Swap motor power wires
2. Update motor control set points
3. On Motor controller: Swap limit switch lines (Conenctors 2 and 3 swapped around)
4. Added extensions for limit switches to ensure good point of contact

Changes made to software:
1. Altered distance calc
2. Altered Up/Down limits check
3. Altered Rod remove algorithm
4. Changed leadscrew value
5. Added UNITID/IND/DISTRICT/LONG/LAT for file name
6. Changed ramp up/down settings to make motor stop quicker and put less stress on limit switches.
7. "Cancel" on pop ups should now work!
8. Added user input for UNITID, IND,DIST, LONGITUDE,LATITUDE at start up. Just warning to enter when started. Will not run test without detail entered.

Changes still needed:
1. Level action micro switches as limit stops are too 'hard'
2. Need Leadscrew mm per rotation movement. Assumption is that its 10.0mm/rev.
3. Calibrate load cell
4. Calibrate distance measurement